K

Linings/Sheathing/Dry partitioning
K30 Panel partitions

Polar Double Glazed partition system

• Manufacturer: Komfort Workspace

- Web: www.komfort.com

- Tel: +44 (0)1403 390 300

- Fax: +44 (0)1403 218 828

- Address: Ashurst, Broadlands Business Campus, Horsham, West Sussex, RH12 4QP

• Agent: Allied Workspace Ltd

- Tolka Valley Business Park, Glasnevin, Dublin 11

- Contact: Tim Evans

- Mobile +353 87 2262228

- Tel: +353 1 8532222

- Email: timevans@allied.ie

• Product reference: Polar Double Glazed partition system /Polar-Tec Double Glazed

partition system.

• Location: As drawing ___

• Layout: As drawing ___

• Performance of completed system:

- Fire resistance to BS 476-22: Non-rated /30 minutes integrity /30 minutes integrity, 30

minutes insulation.

- Fire propagation to BS 476-6: Non-rated /Class 0 (England / Wales / N. Ireland) /Low

risk (Scotland).

- Spread of flame, to BS 476-7: Class 1

- Acoustic insulation to BS EN ISO 140-3: ___ dB (Rw)

• Partition height: To suit floor to ceiling height of ___

- Deflection allowance: Not required /Required

• Glazed panels:

- Glass: 10 mm toughened + 6 mm toughened glass /10 mm toughened + 8 mm

toughened glass /2 x 10 mm toughened glass /10 mm toughened + 12 mm

toughened glass /10 mm toughened + 12.8 mm Stadip acoustic glass /10 mm

toughened glass + 12 mm Komfort intumescent toughened

- Glazing joints:

- In-line: Ghost post and dry joint (DGP2 + DGP15) /Silicone         - 90°Corner junction:

Bubble joint (SJ34) /Curved post (M07) /Ghost post (DGP2).

- Manifestation:

• Framework finish: Kolourframe stove enamelled /Kolourframe polyester powder coated

/Komfort hammer finish /Satin anodized aluminium.

- Colour: BS 4800 ref ___ /RAL ref ___

• Incorporated features:

- Door:

- Fire rating: 30 minutes /Non-rated

- Type: Glass /Hollow core /Solid core - Size: 1981 mm x 838 mm x 44 mm /2040 mm x

826 mm x 44 mm /___ mm x ___ mm x ___ mm

- Finish:

- Vision panel:

- Overpanel:

- Ironmongery:

- Blind:

- Type: Perforated slat,15mm /Perforated slat, 25mm /Plain slat, 15 mm /Plain slat, 25mm

- Finish: Brushed aluminium /Polished aluminium /Satin anodized aluminium, colour as

partition framework /Satin anodized aluminium, colour ___

• Accessories: 1-gang/ 2-way, double insulated rocker switch /PIR detector /Switch face

plate, satin anodized aluminium, colour ___ /Ultrasonic detector

• Installation: Frame installation and glazing to be carried out by Komfort Workspace

approved installer.