K

Linings/Sheathing/Dry partitioning
K30 Panel partitions

Polar Ls90 partition system

• Manufacturer: Komfort Workspace

- Web: www.komfort.com

- Tel: +44 (0)1403 390 300

- Fax: +44 (0)1403 218 828

- Address: Ashurst, Broadlands Business Campus, Horsham, West Sussex, RH12 4QP

• Agent: Allied Workspace Ltd

- Tolka Valley Business Park, Glasnevin, Dublin 11

- Contact: Tim Evans

- Mobile +353 87 2262228

- Tel: +353 1 8532222

- Email: timevans@allied.ie

• Product reference: Ls90 System

• Location: As drawing ___

• Layout: As drawing ___

• Performance of completed system:

- Fire resistance to BS 476-22: Non-rated

- Fire propagation to BS 476-6: Non-rated /Class 0 (England / Wales / N. Ireland) /Low

risk (Scotland)

- Spread of flame, to BS 476-7: Class 1

- Acoustic insulation to BS EN ISO 140-3: ___ dB (Rw)

- Partition height: To suit floor to ceiling height of ___

- Deflection allowance: Not required /Required

• Panel type:

- Solid: Laminated MDF /Powder coated MDF /Pre-vinyled MDF /Veneered MDF /Powder

coated steel faced plasterboard /Pre-vinyled plasterboard /As drawing ___ /As

schedule ___

- Glazed: Flush, double /Flush, triple /As drawing ___ /As schedule ___

• Panel widths: ___ mm /As drawing ___

• Solid panel finish/ colour:

- Finish: Epoxy polyester powder coated /___ 1370 mm wide wallcovering, factory

laminated /___ 1600 mm wide wallcovering, factory laminated /___ veneer – pre

finished /___ laminate

- Colour: BS 4800 ref ___ /RAL ref ___

• Junction, corner and fair end details: Contractor's choice /Manufacturer's standard

• External frames:

- Finish: Brushed aluminium /Epoxy polyester powder coated

- Colour: BS 4800 ref ___ /RAL ref ___ /Self coloured

• Manifestation:

• Integral venetian blinds: Not required /15 mm perforated slat /15 mm plain slat /25 mm

perforated slat /25 mm plain slat

- Finish: Satin anodised /Brushed aluminium /Polished aluminium

• Doorsets: Solid core, 44 mm thick

- Single doorsets:

- Height x width: Full height x ___ mm width /Height ___ mm x ___ mm width

- Double doorsets:

- Height x width: Full height x ___ mm width /Height ___ mm x ___ mm width

- Overpanel, meeting stile and edge details: Matching overpanel /Rebated edge meeting

stiles /Rebated edge overpanel /Square edge

meeting stiles /Square edge overpanel

/Manufacturer's standard

- Doors:

- Finish: Laminate ref ___ /Veneer ref ___, pre-lacquered /Veneer ref ___, on-site finish

- Vision panels:

- Number:

- Shape: Not applicable /Circular /Rectangular /Square

- Size: Not applicable

- Location within doorleaf: Not applicable

- Glazing: Not applicable /Non fire safety rated (class ‘B’) clear, 6.4 mm thick laminated

glass /'Pyran’ 30 minute clear fire/ safety rated (class ‘A’) 6 mm thick glass /‘Pyrobelite’

30 minute clear fire/ safety rated (class ‘A’) 6 mm thick glass /‘Pyrocet’ 30 minute clear

fire/ safety rated (class ‘A’) 6 mm thick glass

• Ironmongery: Manufacturer's standard

• Cable management and electrical outlets:

- Switch face plates: Single switch face plate to contrast with partition colour /Single

switch face plate in polished stainless steel /Double switch face plate to contrast with

partition colour /Double switch face plate in polished stainless steel /As section ___

• Accessories:

• Other requirements:

• Installation: Frame installation and glazing to be carried out by Komfort Workspace

approved installer.